## Slide 1: Overview
Calculate Performance from Weather Measurements
  Use various softwares: SAM, bifacialVF/br+Pvlib, and PVSyst
  Explore different SR for albedometer and POA sensors, and different sensor locations effects
  Compare at middle point with measured field POA and then with Performance data
2) Calculate Performance from POA measurements
  Use various softwares: SAM, bifacialVF/br+Pvlib, and PVSyst
  Explore using GFront only, or Gfront+Grear from various sensors including different SR, locations, he Reference Module, and the Rotating Albedometer approach
Front Only POA
Hydra
Measured Front and Rear POA
Reference Module
HYDRA
Rotating Alb.
2) Performance comparison
CM11 Albedo
?
IMT Albedo
1) Irradiance Comparison (Middle step)
Uncertainties Distribution?
Rotating Alb.
CM11 Albedo
?
IMT Albedo
DHI + DNI
GHI
GHI
DHI + DNI
1) Performance Comparison (end step)
Measured Front and Rear POA

## Slide 2: Study suggestion:
1 year data from May 2021 to May 2022
  Many system interruptions starting May 22 for measurements.
  Only ~3.5 months of Rotating Albedometer (Method 3) data. Could use all the way to August
Select also sets of 3 days between Feb. 22 to May 22 to look closer at the comparison for ALL methods for ‘capacity testing’
  Choose 1 set of nice clear sky days, and 1 set that has funky snow.
Notes:
  Doing 3 days or doing 1 year is the same for most softwares; we run the full year and then single out into the chosen 3 day sets for plots or analysis.
    More data: better bias reduction, but more RMSE.
  Technically ~3 years of data available for 2 bifacial rows, and 1 monofacial string level comparison.
  Nov. 2020 one extra bifacial row added (total of 3 bifacial rows open data available)
  Spectrum Responsivity effects and ‘location’ of sensors effects can be evaluated and interpreted as ‘uncertainty’ for all the variations of methods.

## Slide 3
Combinations of Measurements and Modeling Steps

## Slide 4
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 0a
Compare to Measured
Performance

## Slide 5
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 0b
Compare to Measured
Performance

## Slide 6
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 1a
Compare to Measured
Performance

## Slide 7
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 1b
Compare to Measured
Performance

## Slide 8
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 1c
Measure Front POA
Compare to Measured
Performance

## Slide 9
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 2a
Measure Front POA
Compare to Measured
Performance

## Slide 10
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Compare to Measured
Performance
Method 2b
Measure Front POA
Measure Rear POA

## Slide 11
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 3?
Measure Front POA
Measure Rear POA
Compare to Measured
Performance
Rotating Albedometer

## Slide 12
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 4a
Measure Front POA
Measure Rear POA
Compare to Measured
Performance
Rotating Albedometer
Reference Module Rear Irradiance
Reference Module Front + Rear Irradiance (HYDRA)

## Slide 13
DNI
DHI
GHI
Albedo Data (GHI + GRI)
Model Front Irradiance
Model Rear Irradiance
Model Performance
Method 4b
Measure Front POA
Measure Rear POA
Compare to Measured
Performance
Rotating Albedometer
Reference Module Rear Irradiance
Reference Module Front + Rear Irradiance (HYDRA)